## Slide 1: Construction
Topic: Modern Methods of Construction
Route: Construction
Lesson 1 & 2: Introduction to Modern Methods of Construction
Notes: Image © Shutterstock/Amorn Suriyan

## Slide 2: In these lessons, we will:
describe what is meant by Modern Methods of Construction (MMC);
explain why MMC is used;
outline the impact that using MMC has on job roles in the industry;
discuss the use of MMC in placements (if applicable).
Skills:
CS1 Participate in group and class discussions to examine concepts and approaches to produce solutions to construction problems
CS1 Synthesise information from given case studies, construction projects or site visits
General competencies:
English:
E2 Present information and idea
E4 Summarise information/ideas
E6 Take part in/leading discussions
Digital:
D3 Communicate and collaborate
Lesson 1 & 2: Introduction to Modern Methods of Construction
Introduction

## Slide 3: Class discussion
What do you already know about MMC?
Lesson 1 & 2: Introduction to Modern Methods of Construction
Introduction
Notes: Image © Shutterstock/vilax

## Slide 4: What is MMC?
MMC is a way of combining manufacturing processes, new technologies and new methods of building to be more efficient and effective when compared to traditional forms of construction.
MMC involves moving away from traditional on-site construction and towards off-site manufacture in factories, to increase the quality of buildings.
Lesson 1 & 2: Introduction to Modern Methods of Construction
Introduction
Notes: Image © Shutterstock/Bilanol

## Slide 5: Types of off-site construction
Volumetric systems
Lesson 1 & 2: Introduction to Modern Methods of Construction
Panelised systems
Sub-assemblies and components
Introduction
Notes: Image © Shutterstock/Jarama
Image © Shutterstock/Bilanol
Image supplied by McVeigh build@mcveighoffsite.com

## Slide 6: Volumetric construction
Volumetric construction uses three-dimensional modules produced in controlled factory conditions prior to final installation.
Volumetric modules can be brought to the final site in a variety of forms ranging from basic structure only, to one with all internal and external finishes and services installed, ready for installation.
The system includes structural performance – the structural load-bearing properties of the building are designed into the modules.
Lesson 1 & 2: Introduction to Modern Methods of Construction
Introduction
Notes: Image © Shutterstock/Jarama

## Slide 7: Panelised systems
Flat panel units built in a factory and transported to site for assembly into a three-dimensional structure or to fit within an existing structure.
This includes structural insulated panels (SIP) and other sandwich panels. These consist of two layers of a rigid material bonded to either side of a lightweight core.
Lesson 1 & 2: Introduction to Modern Methods of Construction
Introduction
Notes: Image © Shutterstock/Bilanol

## Slide 8: Sub-assemblies and components
These are smaller elements of off-site construction. They include pre-manufactured components such as:
pre-assembled units, including roof and floor cassettes;
precast concrete sections and cladding panels;
framed panels (timber, steel);
pre-assembled structural steelwork.
Lesson 1 & 2: Introduction to Modern Methods of Construction
Introduction
Notes: Image supplied by McVeigh build@mcveighoffsite.com

## Slide 9: MMC – not just houses
MMC is not just used for building houses and offices. They are also used in the construction of railways and large-scale power stations, for example.
This video demonstrates how MMC has been used in the construction of HS2, the UK’s high-speed rail network.
Lesson 1 & 2: Introduction to Modern Methods of Construction
Introduction
Notes: HS2 tunnel boring machine video: https://youtu.be/sGEMHn01p4g

## Slide 10: Class discussion
How does using MMC compare with traditional construction?
Do you think MMC is important? If so, why/why not?
Do you think MMC will help us meet building regulations? If so, why/why not?
Do you think MMC could help us meet construction targets? If so, why/why not?
How do you think MMC impacts sustainability?
Summary question: Why do we use MMC?
Lesson 1 & 2: Introduction to Modern Methods of Construction
Activity 1

## Slide 11: Overview of MMC
Lesson 1 & 2: Introduction to Modern Methods of Construction
Activity 1
Notes: Overview of MMC video: https://vimeo.com/1069603912

## Slide 12: Mind map
Why use MMC?
Digital compatibilities
Planning
Waste reduction
Environmental benefits
Regulatory control
Quality control
Activity 2
Lesson 1 & 2: Introduction to Modern Methods of Construction
Improved performance
Complete the mind map using L1 & 2 Activity 2 worksheet

## Slide 13: Example mind map
Why use MMC?
Digital compatibilities
Planning
Waste reduction
Environmental benefits
Regulatory control
Quality control
  Project management and design using BIM
  Computer Numerical Control (CNC) panel production
  Useful for social housing due to speed of construction
  Can be issues with lack of individuality between dwellings
  Designed to use full sheets of timber
  Waste produced during manufacturing processes is kept within the factory for easy recycling
  Well-insulated with minimal air gaps – less use of heating via fossil fuels
  Less waste on-site
  Problems with Gas Safe and fireproofing in Building Control
  Standard panels mean prior consultation, therefore it’s easier to meet regulations
  Factory produced panels mean that quality checks are conducted on all materials and completed panels in a controlled environment
Activity 2
Lesson 1 & 2: Introduction to Modern Methods of Construction
Improved performance
  Reduced risk of error
  Digital twins

## Slide 14: Professional roles in MMC
What professional and trade roles in construction would you expect to be involved with MMC?
What would you expect their roles to be?
Lesson 1 & 2: Introduction to Modern Methods of Construction
Activity 3
Notes: Image © Unsplash/Pedro Miranda

## Slide 15: Impact of MMC on job roles
While watching construction professionals discuss their roles in the videos, take notes on the following questions:
  How is the person’s role different using this method compared with traditional methods?
  What extra skills are required to use this method within the role?
  How does this person collaborate with other professionals that they might not work with when using traditional methods?
  How might MMC change their job in the future?
Make notes using L1 & 2 Activity 3 worksheet 1 or 2
Activity 3
Lesson 1 & 2: Introduction to Modern Methods of Construction

## Slide 16: Interview with Architect
Activity 3
Lesson 1 & 2: Introduction to Modern Methods of Construction
Notes: The role of the architect video: https://vimeo.com/1069605995

## Slide 17: Interview with Project Manager
Activity 3
Lesson 1 & 2: Introduction to Modern Methods of Construction
Notes: The role of the project manager video: https://vimeo.com/1069604569

## Slide 18: Interview with Registered Building Inspector
Activity 3
Lesson 1 & 2: Introduction to Modern Methods of Construction
Notes: The role of the registered building inspector video: https://vimeo.com/1069604879

## Slide 19: DfMA overlay to RIBA Plan of Work
Activity 3
Lesson 1 & 2: Introduction to Modern Methods of Construction
Notes: DFMA overlay to RIBA Plan of Work https://www.architecture.com/knowledge-and-resources/resources-landing-page/dfma-overlay-to-the-riba-plan-of-work#available-resources (page 63)

## Slide 20: Make a video
Plan and film a one-minute video that answers the question, ‘How are construction roles different when MMC is involved?’
In small groups, collaborate to:
decide on the script
agree on any images
present this information.
Lesson 1 & 2: Introduction to Modern Methods of Construction
Activity 3
Notes: Image © Pexels/Yan Krukau

## Slide 21: Placement experience showcase
Create a presentation slide show and answer the following questions:
What involvement have you had in your placement role?
How have you worked with other parties to deliver MMC?
Which modern methods of construction have been used on your site?
Include photos where possible.
Lesson 1 & 2: Introduction to Modern Methods of Construction
Plenary
Notes: Image © Shutterstock/Amorn Suriyan

## Slide 22: In these lessons, we have:
described what is meant by Modern Methods of Construction (MMC);
explained why MMC is used;
understood the impact that using MMC has on job roles in the industry;
discussed the use of MMC in placements (if applicable).
Lesson 1 & 2: Introduction to Modern Methods of Construction
Plenary
Skills:
CS1 Participate in group and class discussions to examine concepts and approaches to produce solutions to construction problems
CS1 Synthesise information from given case studies, construction projects or site visits
General competencies:
English:
E2 Present information and idea
E4 Summarise information/ideas
E6 Take part in/leading discussions
Digital:
D3 Communicate and collaborate

## Slide 23
Key terms
Write definitions for:
  MMC
  Off-site construction
  Volumetric construction
  Panelised systems
  Sub-assemblies and components
  DfMA
  BIM software
  Digital twin
Consolidation
Lesson 1 & 2: Introduction to Modern Methods of Construction
Notes: Image © Shutterstock/brizmaker